## Slide 1: TPAC1.2 Results
Jamie Crooks
1st June 2009

## Slide 2: Status
TPAC1.2 received
WAFERS | EPI | SUBSTRATE | DPW | DICED QTY
3 | 12 | STD | YES | 75
3 | 12 | STD | NO | 75
3 | 12 | HI RES | YES | 75
3 | 18 | HI RES | YES | 75

## Slide 3: Status
7 chips now bonded, 5 more in progress
  0 power-ground shorts 
  5 usable sensors today
PCB | WFR | VARIANT | ALIGNMENT | TEST | NOTES
50 | 3 | 12u +DPW | LASER | Configuration errors (all cols) | 
29 | 3 | 12u +DPW | LASER | Ok | Paul/CALICEDAQ1
43 | 3 | 12u +DPW | LASER | Ok | Marcel/55Fe
41 | 3 | 12u +DPW | LASER | Ok, with configuration errors (col 53 only) | 
21 | 9 | 12u HIRES + DPW | LASER | Ok, with configuration errors (col 148 only) | 
44 | 2 | 12u +DPW | CENTER | Ok | 
42 | 2 | 12u +DPW | CENTER | Spill fails | 
47 |  | 12u +DPW | CENTER |  | 
46 |  | 12u +DPW | CENTER |  | 
45 |  | 12u +DPW | CENTER |  | 
23 |  | 12u +DPW | CENTER |  | 
48 |  | 18u HIRES + DPW | LASER |  | 

## Slide 4: Per-Pixel threshold scans (noise)
Randomly selected single pixel in each region
Noise is Gaussian 
  Pixel shielding added on metal 2 appears to help
  Coupling/oscillation at low thresholds is not evident

## Slide 5: Single pixel trim scan
Trims 0,2,4,6,8,10,12,14,16,18,20,22,24…
The trim range still needs to be set up correctly
Was never done for TPAC1.1 which had the larger #bits
May involve a resistor value change
Once per-pixel spread is known I can set this
Sooner the better (for modifying PCBs)
Currently the range should be twice that on TPAC1.0 with 4x resolution

## Slide 6: Pixel addresses (noise)
TPAC1.1
  Addressing bug
TPAC1.2
  Full addresses restored